## Slide 1: Firmware

## Slide 2
batt
ls
sens
CO
CO2
PMS
T/H/P/voc
NOx
WEATH
net
Lorawan
3G
wifi
sensor_ops
if_ops
can5_mod
master (main)
config
config_ops
sleep
sleep_ops

## Slide 3: INterfaces
sensor_ops
if_ops
can5_mod
config_ops
sleep_ops
Can5mod: used as “threads”, round robin scheduling, runs process()
Network: TX/RX operations
Sensor: Configure, Preheat and Acquire sensors
Config: Used in Config mode, collect properties construct property tree and show webpage. Save webpage config
Sleep: Poll modules for max time sleep, triggers sleep

## Slide 4: Todo
Change the module to be used with freeRTOS
Process is substituted by event_handler
Add a scheduler that allows modules to set callbacks
  The scheduler is responsible for keeping the device in deep sleep and setting timeouts for the next callback
  The scheduler enables external wakeup sources like GPIO interrupts (e.g. network event)
  RTC Data Area can be used to store variables
  ULP can be used to read sensors or GPIO interrupts -> wake
Write Lora library for murata lib
Write HW abstraction to use with multiplexed ports

## Slide 5: FreeRTOS
Only 1 core We must be Low Power
Threads? Probably not necessary if we use a scheduler with callbacks and RTC to wakeup.
  Thread sleep? vApplicationIdleHook()? https://www.esp32.com/viewtopic.php?t=12477
  https://lastminuteengineers.com/esp32-sleep-modes-power-consumption/
Light sleep 800mA
Deep sleep 10uA